## Slide 1
IMESA Southern Cape Quarterly Meeting.
smart Metering
August 2016
MARK CAPPER

## Slide 2
Mechanical ‘dumb’ meter
Electronic meter with / w/o integrated AMR
Mechanical with external smart modules
Smart hybrid meter with integrated smart
Meters Are Evolving ……….
Mechanical
Hybrid
Electronic

## Slide 3
Trends In Water Metering
“To measure is to know” – Lord Kelvin
“every drop” of water that is sourced needs to be accounted for throughout the supply chain
Trends - reliable and accurate basic metering and solutions that add value:
  Good Revenue Meters – reliable and accurate meters – good volumetric and hybrid meters
  Water Management Devices (WMD) – FBW, shut-off valve
  Prepayment (STS) – similar system to electricity PP, costs
  Automatic Meter Reading (AMR) – walk-by / drive-by for value and consistent readings, Cellular / LoRa AMR. Logging
  Meter Data Management (MDM) – Smart Metering, Cloud-based, Internet of Things (IoT), Mobile Applications – Billing, Leak Detection, Logging
For value - a reliable and accurate good revenue generating meter
Water meters are the cash registers
for water suppliers

## Slide 4
Water Management Devices (WMD)
Electronically controlled valve connected to a pulse output water meter
  The delivery of an allocation of a finite or pre-negotiated daily or monthly water allowance (free basic water)

## Slide 5
Prepayment Solutions
Domestic Water Dispensers are designed for individual households to control the dispensing of pre-paid quantities of water, available in Dallas token or STS prepayment (similar to electricity prepayment)
The prepayment meter is programmable to issue the minimum 6kl of free basic water (FBW) and thereafter it has a step tariff function which then charges for every kl used
There are two ways of dispensing the 6kl of free water:
200 litres of water per day or
6kl of water from the first day of the month until the allocation is reached thereafter water credit must be purchased

## Slide 6
Automatic Meter Reading (AMR)
AMR (Automated Meter Reading) is the fundamental technology that enables:
Collection of data from meters via one-way communications
Integration of information back into a database for billing or data analysis
Eliminates manual readings, allowing billing to be based on actual consumption rather than on an estimate, giving customers better control of their water consumption

## Slide 7
Direct communication between meter and PC or Hand Held
Meter data visible in “real time”
Can be incorporated within customers billing (R & c)
Events: leak, tamper, burst
Simpler and lower cost e.g. Walk-by / Drive-by Vs Fixed Network
“Continuous” AMR = Logging
Direct
AMR - Description

## Slide 8
Advanced Metering Infrastructure (AMI)
AMI (Advanced Metering Infrastructure) refers to intelligent metering systems which:
Measure, collect, and analyse consumption, leakage and other available data from advanced devices or smart meters on demand
Utilise various communication media on request or on a pre-defined schedule (two-way communication)

## Slide 9
Mesh network between all meters and Management software
Real time alerts via sms or
email
Full 2-way communication
Full site inspection to be
done before hand
More advanced system but
at higher cost
AMI - Description

## Slide 10: LoRa Technology with Mobile App
LoRa™ RF technology is a long range and secure, bidirectional communication.
Low Power WAN
Battery operated
Gateway/Concentrator (star topology)
Ideal for Internet of Things (IoT), metering, security, asset tracking, and machine-to-machine (M2M) applications
Features:

## Slide 11: LoRa Technology with Mobile App
Two-way communication so unit can be redesigned to control valve function on the fly
Gateways transfer bundled data to Network Servers on GSM networks via GPRS connection
Over the air updates
Compact size
Extended end-device battery life ±5 years
Low cost end-device
Low cost gateway device. Powered by 10W solar panel + 12V 7.2AH battery (1 Gateway servicing 1000+ devices)
No cost per message from end-devices to gateway
Extremely low server monthly service fee per end-device connected
Elster create their own LoRa network, hence any Elster LoRa device (Electricity meters etc.) can connect to same network.

## Slide 12: LoRa Technology with Mobile App
Graphical Illustration
Meter with Remote reading device
Webserver
App on Consumer mobile
Municipality

## Slide 13
AMR / AMI
Meters
Communication
Head end
GPRS Ethernet
ComServerJ
ERM2
GPRS Ethernet
Walk-by or Drive-by
Fixed Network
Fixed Network

## Slide 14
Technology Challenges
Challenges faced with new technologies and solutions:
Many require some source of energy – LCD display, radio, valve, etc.
  Battery life expectancy (“up to x years”) – also depends on type and frequency of energy requirement
Communications technology challenges
  Type of comms / protocols – cellular, satellite, radio, wifi, internet / ANSI, IEC protocols / fixed wireless, mesh network
  Cost effectiveness – Upfront and monthly costs, operational and maintenance costs
  Reliability
  Comms. Distances (“up to xx m line of sight”)
  Software systems
  Interoperability – complex system integration, etc.
Data management and analysis
Data security / Privacy – smart meters are becoming too smart (cybersecurity)
Health and safety concerns – EM emissions
Lack of proven savings / Business case is critical

## Slide 15
Metering Solutions
WMD
(Upgradeable)
Remote Shut-Off
(Trickle)
Prepayment
Dallas Token
STS
AMR
Walk-By
Fixed
(Cellular,Wi-Fi)
AMI
2-Way Comms
1-Way Comms
(from Meter)
1-Way Comms
(to Meter)
Shut-Off Valve
There’s no
“One size fits all solution”
LoRa

## Slide 16
SMART METERING

## Slide 17
Smart Meters
Elster Q200 Electronic Meter
“SmartMeter” is an Elster Water Trade Mark

## Slide 18
Smart Meters
Everyone wants “Smart” meters
Word “Smart” loosely used as a marketing term (not technical term) to promote a silver bullet “solution to all utility problems”
No clear definition of a “Smart” meter in Water Industry

## Slide 19
Simplified Definition of Smart Meters
A Smart Meter is a measuring device that, as a minimum requirement, is capable of communicating data to a remote interface at regular intervals
In it’s basic form, smart metering is Automatic Meter Reading (AMR)
Technology is mature and can unlock benefits of data

## Slide 20
Benefits of Smart Meters
Benefits to Utility:
Read meter remotely / no access required to properties
Improve meter reading performance – efficiency and accuracy
Tamper detection possible
Proactive leak detection possible
Reduced water pumping through reduced water leakage
Benefits to Consumer:
Provide greater information to customers in relation to their consumption, which enables them to make informed, proactive decisions about their water usage
Provide information to customers that allow them to identify household leakages
Support more frequent and accurate customer billing

## Slide 21
Lean Smart solutions

## Slide 22
Why does everyone want Smart Metering?
Smart metering will solve all our problems
It’s our “silver bullet” – leaks, high non-revenue (NRW) water, billing, non-payment, tampering
The investment is worth it if the problems go away
Smart metering is the latest technology in metering

## Slide 23: Smart Meter Financial Feasibility
Is there a financially feasible solution that can eliminate or minimise the challenges that Utilities face?
“Lean Smart” Metering (Do more with less)
– Smarter solution that excludes the high costs associated with “smart” electronics added to each meter
e.g. 100,000 meters require an additional ZAR 70.7M to upgrade good meters to become basic “smart” meters
– Smart meter projects are not always financially feasible
Cost Comparison: Smart Metering Vs Basic Metering *
Product cost only
Smart costs are for basic Walk / Drive-by AMR

## Slide 24
Lean Smart Metering Solution
Meter Reading and Billing Smart Phone App
Seamless digital meter reading solution that uses affordable smartphones to collect meter information, readings, pictures and GPS co-ordinates for water or electricity connections
Meter Reader or Consumer inputs meter reading into smart phone App, data read by online platform
Automated SMS sent to consumer with:
  Opening Reading
  Closing Reading
  Water / Electricity usage in period
  Invoice amount / Bill
Online payment option via separate App (Square Cash)
Replaces paper forms and adds functionality such as time-stamped pictures of the meter reading and GPS co-ordinates
Mobile App ready for implementation!
Square Cash

## Slide 25
Lean Smart Metering Solution
Meter Reading and Billing Smart Phone App
Lean Smart Metering can resolve the majority of challenges experienced by utilities:
*
* Assumes that reliable and accurate meter is used

## Slide 26
Water is very Cheap
* Average consumer cost of water, Jhb rates, 30kl consumption per month
Difference > 1,000 X
> 600 X

## Slide 27
Water is very Cheap

## Slide 28
Water
Losses
Authorized
Consumption
Real
Losses
Apparent
Losses
Unbilled
Authorized
Consumption
Billed
Authorized
Consumption
Non-
Revenue
Water
Revenue
Water
Leakage & Overflows at Storage
Billed Unmetered Consumption
Billed Metered Consumption
Billed Water Exported
Leakage on Service Lines
Leakage on Mains
Customer Metering Inaccuracies
Unauthorized Consumption
Unbilled Unmetered Consumption
Unbilled Metered Consumption
Systematic Data Handling Error
Source: IWA Water Balance
36.8% (1.58bn m3)
R 9,5bn
IWA Water Balance
±20%
R 5,2bn

## Slide 29
Non-Revenue Water (NRW) - Metros
Source: DWS 2015 No Drop Report
Metro NRW weighted average = 42.8% (SA = 36.8%)
Metro water usage approx. 40% of SA total
Water scarcity is not the real problem
High NRW provides opportunity

## Slide 30
High NRW = Opportunity!

## Slide 31
Non-Revenue Water (NRW) - Metros
NRW in Tokyo = 3%, Sydney = 12%
High NRW is also opportunity
Minimise water losses:
  Pressure management,
  Active leakage control,
  Asset management,
  Speed and quality of repairs
A 10% reduction in system input volume (SIV) and reducing NRW to 25% can generate approximately ZAR 2bn additional income through reduced water purchases and increased water sales
(plus 10% energy savings due to less pump hours)
Source: DWS 2015 No Drop Report

## Slide 32
Impact of Leak Run Time
Leak Run Time (days)
Leak Flow Rate (m³/day)
A
L
R
A Awareness Time
L Location Time
R Repair Time
(A + L + R) [d] x flow rate [m³/d] = Water Lost [m³]
Opportunity
Leak Run Time x Flow Rate = Volume of Water Lost

## Slide 33
Impact of Leak Run Time
Leak Run Time (days)
Leak Flow Rate (m³/day)
A
L
R
A Awareness Time
L Location Time
R Repair Time
A
L
R
Volume of Water Saved
Reduce Awareness Time
(A + L + R) [d] x flow rate [m³/d] = Water Lost [m³]
Leak Run Time x Flow Rate = Volume of Water Lost

## Slide 34
Impact of Leak Run Time
Leak Run Time (days)
Leak Flow Rate (m³/day)
A
L
R
Volume of Water Saved
(A + L + R) [d] x flow rate [m³/d] = Water Lost [m³]
(1.5 + 0.1 + 0.2) [d] x 240 [m³/d] = 432 [m³]
(0.2 + 0.1 + 0.2) [d] x 240 [m³/d] = 120 [m³]
Volume of Water Saved = 432 - 120 = 312 [m³]
Value of Water Saved = 312 [m³] x 32.27 [R] = R 10 068 * At Jhb. rates 2016/7
R
L
A
0.2 Days
1.5 Days
0.1 Days
0.2 Days
R
Value of Water Saved x 500 Leaks = 500 x R 10 068 = R 5,034M
Volume of Water Saved

## Slide 35
War on Leaks
President Jacob Zuma announced at the State of the Nation
Address (SONA) 2015:
“Let me Honourable Speaker and Chairperson urge all in the country to conserve water. Every drop counts. The country loses seven billion rand a year to water losses. To mitigate this challenge, Government through the Department of Water and Sanitation will train fifteen thousand artisans and or plumbers who will fix leaking taps in their local communities.”
Phase 1 - September 2015 with 3000 trainees - plumbing, instrumentation, fitter and turner, electrical, welding and water agents. Workplace training commenced in May 2016.
Phase 2 - 7000 trainees as of the 1st of July 2016.

## Slide 36
High volume of water leakage (NRW = 36.8%)
– also opportunity.
How can leakage be reported (Awareness Time) as soon as possible to minimise water lost?
Millions of South Africans carry with them a sophisticated tracking device – cellphone.
Solution - Water Management App.
Allow anyone to actively report water issues via the App e.g. water leaks, water quality, pressure problems, infrastructure theft, etc. instantly and conveniently – from their phones, from wherever they may be.
To report leak, open App, one tap – will allow for reporting of leak (or other water issue) and pin point position utilising GPS co-ordinates.
Lean Smart Management Solution
Water Leakage Reporting via Smart Phone

## Slide 37
The cellular App:
Allows the Utility to dynamically respond to the issue logged (quickly respond to leaks and reduce non-revenue water), and
Plot and record water issues against geographic locations.
This framework could tightly integrate core operations (possibly including War on Leaks Teams) – issuing tasks to repair teams and monitoring their progress in real time, leading to increased efficiencies and more automated workflows.
Convenient, easy to use, cost–effective tool to reduce water wastage.
Will also raise awareness of water use.
Mobile App can be complete within 4 weeks!
Lean Smart Management Solution
Incident Reporting Smart Phone App

## Slide 38
Smart Metering – Conclusions
Do smart metering projects really have a reasonable and feasible financial payback?
It’s been financially a very bumpy ride for many smart metering projects
There is “no one size fits all” solution in metering or Smart metering:
  Focus on selecting the right investment
  Use tools and technology to do more with less (“Lean Smart Solutions”)

## Slide 39
Conclusion
There’s no “Once size fits all” solution in metering
A Reliable and Accurate water meter is the source which enables:
  Informed and optimised data management analysis and decisions e.g. water balance, leak detection, water losses, non-revenue water, logging
  Accurate billing and enhanced revenue collection
Lean Smart metering solutions can provide a more cost effective and efficient solution to solving many challenges

## Slide 40
Thank you
Mark Capper
mark.capper@honeywell.com
+27-21-511-8465/6
www.Honeywell.com
www.elster.com